## Slide 1: A Mostly-Clean DRAM Cache for Effective Hit Speculation and Self-Balancing Dispatch
Jaewoong Sim Gabriel H. Loh Hyesoon Kim
Mike O’Connor Mithuna Thottethodi

## Slide 2: Outline
Motivation & Key Ideas
  Overkill of MissMap (HMP)
  Under-utilized Aggregate Bandwidth (SBD)
  Obstacles Imposed by Dirty Data (DiRT)
Mechanism Design
Experimental Results
Conclusion

## Slide 3: Die-Stacked DRAM
Die-stacking technology is NOW!
Q: How to use of stacked DRAM?
Two main usages
  Usage 1: Use it as main memory
  Usage 2: Use it as a large cache (DRAM cache)
Same Tech/Logic
(DRAM Stack)
Processor Die
Hundreds of MBs On-Chip Stacked DRAM!!
Credit: IBM
Through-Silicon Via
(TSV)
This work is about the DRAM cache usage!

## Slide 4: DRAM Cache: State of the Art
DRAM Cache Organization: Loh and Hill [MICRO’11]
  1st Innovation: TAG and DATA blocks are placed in the same row
    Accessing both without closing/opening another row => Reduce Hit Latency
  2nd Innovation: Keep track of cache blocks installed in the DRAM$ (MissMap)
    Avoiding DRAM$ access on a miss request => Reduce Miss Latency
3 tag blocks
29 data blocks
Row Decoder
Sense Amplifier
DRAM Bank
…
Row X
DRAM (2KB ROW, 32 blocks for 64B line)
MissMap
Memory Request
Not Found!
Do not access DRAM$
Check MissMap
for every request
Record the existence of the cacheline!
Found!
Send to DRAM$
On a hit, we can get the data from the row buffer!
Tags are embedded!!
However, still has some inefficiencies!

## Slide 5: Problem (1): MissMap Overhead
MissMap is expensive due to precise tracking
  Size: 4MB for 1GB DRAM$
  Latency: 20+ cycles
Miss Latency (original)
Hit Latency (original)
ACT
CAS
TAG
Off-Chip Memory
MissMap
ACT
CAS
TAG
DATA
Where to architect this?
MissMap
Off-Chip Memory
Hit Latency (MissMap)
ACT
CAS
TAG
DATA
MissMap
Miss Latency (MissMap)
Reduced!
20+ cycles
20+ cycles
Increased!
Added to every memory request!

## Slide 6: Problem (1): MissMap Overhead
Avoiding the DRAM cache access on a miss is necessary
  Question: How to provide such benefit at low-cost?
Possible Solution: Use Hit-Miss Predictor (HMP)
Cases of imprecise tracking
  False Positive: Prediction: Hit, Actual: Miss (this is OK)
  False Negative: Prediction: Miss, Actual: Hit (problem)
Observation: DRAM tags are always checked at installation time on a DRAM cache miss
  False negative can be identified, but
HMP would be a more nice solution by solving dirty data issue!
Dirty Data 
Less Size 
Must wait for the verification of predicted miss requests!

## Slide 7: Problem (2): Under-utilized BW
DRAM caches ≠ SRAM caches
  Latency: DRAM caches >> SRAM caches
  Throughput: DRAM caches << SRAM caches
Hit requests often come in bursts
  SRAM caches: Makes sense to send all the hit requests to the cache
  DRAM caches: Off-chip memory can sometimes serve the hit requests faster
Stacked
DRAM$
Off-chip
Memory
Another Hit Requests
Req. Buffer
Req. Buffer
Always send hit requests to DRAM$?
Off-chip BW would be under-utilized!

## Slide 8: Problem (2): Under-utilized BW
Some hit requests are also better to be sent to off-chip memory
  This is not the case in SRAM caches!
Possible Solution: Dispatch hit requests to the shorter latency memory source
  We call it Self-Balancing Dispatch (SBD)
Now, we can utilize overall system BW better 
  Wait. What if the cache has the dirty data for the request?
Solving under-utilized BW problem is critical
  But, SBD may not be possible due to dirty data!
Dirty Data! 
Seems to be a simple problem 

## Slide 9: Problem (3): Obstacles by Dirty Data
Dirty data restrict the effectiveness of HMP and SBD
  Question: How to guarantee the non-existence of dirty blocks?
  Observation: Dirty data == byproduct of write-back policy
Key Idea: Make use of write policy to deal with dirty data
  For many applications, very few pages are write-intensive
Solution: Maintain a mostly-clean DRAM$ via region-based WT/WB policy
  Dirty Region Tracker (DiRT) keeps track of WB pages
2
2
0
0
9
0
8
1
0
# of writes
Clean or Dirty?
4KB regions (pages)
0
0
9
0
8
1
0
4KB regions (pages)
Write-Back
Write-Through
Clean!!
But, we cannot simply use WT policy!

## Slide 10: Summary of Solutions
Problem 1 (Costly MissMap) Hit-Miss Predictor (HMP)
  Eliminating MissMap + Look-up latency for every request
Problem 2 (Under-utilized BW) Self-Balancing Dispatch (SBD)
  Dispatch hit request to the shorter latency memory source
Problem 3 (Dirty Data) Dirty Region Tracker (DiRT)
  Help identify whether dirty cache line exists for a request
These are nicely working together!
Dirty Request?
DRAM$ Queue
DRAM Queue
Predicted Hit?
E(DRAM$) <
E(DRAM)
YES
NO
NO
YES
NO
YES
DiRT
HMP
SBD
Mechanism
START
E(X): Expected Latency of X

## Slide 11: Outline
Motivation & Key Ideas
Design
  Hit-Miss Predictor (HMP)
  Self-Balancing Dispatch (SBD)
  Dirty Region Tracker (DiRT)
Experimental Results
Conclusion

## Slide 12: Hit-Miss Predictor (HMP)
Goal: Replace MissMap with lightweight structure
  1) Practical Size, 2) Reduce Access Latency
Challenges for hit miss prediction
  Global hit/miss history for memory requests is typically not useful
  PC information is typically not available in L3
Our HMP is designed to input only memory address
Question: How to provide good accuracy with memory information?
Key Idea 1: Page (segment)-level tracking & prediction
  Within a page, hit/miss phases are distinct
High Prediction Accuracy!

## Slide 13: HMPregion: Region-Based HMP
Two-bit bimodal predictor per 4KB region
  A lot smaller than MissMap (512KB vs 4MB for 8GB physical memory)
  Can we further optimize the predictor?
Key Idea 2: Use Multi-Granular regions
  Hit-miss patterns remain fairly stable across adjacent pages
Chart: #Accesses to the page
Miss
Phase
Hit
Phase
Miss
Phase
Hit
Phase
Increasing on misses
Flat on hits
A single predictor for regions larger than 4KB
Needs a few cycles to access HMP
A page from leslie3d in WL-6

## Slide 14: HMPMG: Multi-Granular HMP
FINAL DESIGN: Structurally inspired by TAGE predictor (Seznec and Michaud [JILP’06])
  Base Predictor: default predictions
  Tagged Predictors: predictions on tag matching
  Next-level predictor overrides the results of previous-level predictors
Base: 4MB
2nd-Level: 256KB
3rd-Level: 4KB
Operation details can be found in the paper!
Tracking Regions
Use prediction result from 3rd-level table!
95+% prediction accuracy with less-than-1KB structure!!

## Slide 15: Self-Balancing Dispatch (SBD)
IDEA: Steering hit requests to off-chip memory
  Based on the expected latency of DRAM and DRAM$
How to compute expected latency?
  N: # of requests waiting for the same bank
  L: Typical latency of one memory request (excluding queuing delays)
  Expected Latency (E) = N * L
Steering Decision
  E(off-chip) < E(DRAM_Cache): Send to off-chip memory
  E(off-chip) >= E(DRAM_Cache) : Send to DRAM cache
Simple but effective!!

## Slide 16: Dirty Region Tracker (DiRT)
IDEA: Region-based WT/WB operation (dirty data)
  WB: write-intensive regions. WT: others
DiRT consists of two hardware structures
  Counting Bloom Filter: Identifying write-intensive pages
  Dirty List: Keep track of write-back-operated pages
Counting Bloom Filters
Write Request
Dirty List
Hash B
Hash C
Hash A
TAG
NRU
WB Pages
#writes > threshold
Pages captured in Dirty List are operated with WB!

## Slide 17: Outline
Motivation & Key Ideas
Design
Experimental Results
  Methodology
  Performance
  Effectiveness of DiRT
Conclusion

## Slide 18: Evaluations - Methodology
System Parameters
Mix | Workloads
WL-1 | 4 x mcf
WL-2 | 4 x lbm
WL-3 | 4 x leslie3d
WL-4 | mcf-lbm-milc-libquantum
WL-5 | mcf-lbm-libquantum-leslie3d
WL-6 | libquantum-mcf-milc-leslie3d
WL-7 | mcf-milc-wrf-soplex
WL-8 | milc-leslie3d-GemsFDTD-astar
WL-9 | libquantum-bwaves-wrf-astar
WL-10 | bwaves-wrf-soplex-GemsFDTD
CPU | 
Core L1 Cache L2 Cache | 4 cores, 3.2GHz OOO 32KB I$ (4-way), 32KB D$(4-way) 16-way, shared 4MB
Stacked DRAM Cache | 
Cache Size Bus Frequency Chans/Ranks/Banks | 128 MB 1.0 GHz (DDR 2.0GHz), 128 bits per channel 4/1/8, 2048 bytes row buffer
Off-chip DRAM | 
Bus Frequency Chans/Ranks/Banks tCAS-tRCD-tRP | 800 MHz (DDR 1.6GHz), 64 bits per channel 2/1/8, 16KB bytes row buffer 11-11-11
Workloads

## Slide 19: Evaluations - Performance
Chart: Speedup over no DRAM cache
| WL-1 | WL-2 | WL-3 | WL-4 | WL-5 | WL-6 | WL-7 | WL-8 | WL-9 | WL-10 | AVG.
MM | 1.1159 | 1.2837 | 0.97674 | 1.1473 | 1.0931 | 0.94482 | 1.007 | 0.9494 | 0.98537 | 1.0305 | 1.0487
HMP | 1.1312 | 1.2679 | 0.96226 | 1.0464 | 1.0097 | 0.85586 | 0.96233 | 0.83415 | 0.88065 | 0.99075 | 0.98664
HMP + DiRT | 1.2316 | 1.3663 | 1.043 | 1.1954 | 1.1577 | 1.0115 | 1.0734 | 1.0074 | 1.0572 | 1.0949 | 1.1189
HMP + DiRT + SBD | 1.2378 | 1.5059 | 1.204 | 1.2869 | 1.2672 | 1.1048 | 1.1358 | 1.0977 | 1.0985 | 1.1432 | 1.2027
20.3% improvement over baseline
15.4% more over MM
HMP is worse than MM for many WLs
With DiRT support, HMP becomes very effective!!
MM improves
AVG performance
HMP without DiRT does not work well!
Not better than the baseline
Need verification for predicted miss requests

## Slide 20: Evaluations - Effectiveness of DiRT
Chart: 
| WL-1 | WL-2 | WL-3 | WL-4 | WL-5 | WL-6 | WL-7 | WL-8 | WL-9 | WL-10
CLEAN | 0.859 | 0.261 | 0.899 | 0.426 | 0.538 | 0.914 | 0.821 | 0.878 | 0.954 | 0.785
DiRT | 0.141 | 0.739 | 0.101 | 0.574 | 0.462 | 0.086 | 0.179 | 0.122 | 0.046 | 0.215
Chart: Percentage of writebacks to DRAM
| WL-1 | WL-2 | WL-3 | WL-4 | WL-5 | WL-6 | WL-7 | WL-8 | WL-9 | WL-10
DiRT | 0.22934 | 0.49508 | 0.21046 | 0.53971 | 0.577 | 0.4555 | 0.2249 | 0.76524 | 0.36433 | 0.28404
WB | 0 | 0.47112 | 0.19336 | 0.43014 | 0.43905 | 0.19143 | 0.094026 | 0.51809 | 0.23583 | 0.15674
WT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CLEAN:
Safe to apply HMP/SBD
WT traffic >> WB traffic
DiRT traffic ~ WB traffic

## Slide 21: Outline
Motivation & Key Ideas
Design
Experimental Results
Conclusion

## Slide 22: Conclusion
Problem: Inefficiencies in current DRAM cache approach
  Multi-MB/High-latency cache line tracking structure (MissMap)
  Under-utilized aggregate system bandwidth
Solution: Speculative approaches
  Replace MissMap with a less-than-1KB Hit-Miss Predictor (HMP)
  Dynamically steer hit requests either to DRAM$ or off-chip DRAM (SBD)
  Maintain a mostly-clean DRAM cache with Dirty Region Tracker (DiRT)
Result: Make DRAM cache approach more practical
  20.3% faster than no DRAM cache (15.4% over the state-of-the-art)
  Removed 4MB storage requirement (so, much more practical)
IDEA: Region-Based Prediction!
+ TAGE Predictor-like Structure!
IDEA: Hybrid Region-Based WT/WB policy for DRAM$!

## Slide 23: Q/A
Thank you!